## Slide 1: How it works
Generate short excitation waveform (length L samples), typically noise
Excitation is output & simultaneously fed back into delay line of L samples
  delay line acts to store one period of the signal
Output of delay line fed through filter
  Filter gain must be less than 1 at all frequencies, to avoid unstable feedback loop
  Filter typically a low order, lowpass filter
  Filter characteristics mainly determine harmonic structure of decaying tone.
Filtered output simultaneously mixed back into output & into delay line
loops short waveform through filtered delay line
Noise
burst
Delay
Lowpass filter
destination
+

## Slide 2: Simple implementation
Tuning the string
L is the number of samples of delay
So delay time D=L/fs
  D is the period, i.e. time before it repeats
Fundamental frequency should be 1/D
Want D very small
  10 ms  100 Hz
  5 ms  200 Hz
  2 ms  500 Hz
Noise
Noise
Gain
Delay
Feedback
Gain
destination
+
Variations
Can replace filter with just feedback gain
Can have excitation decay over short time

## Slide 3: Delay line with feedback
Noise
burst
Delay
Feedbackgain
Output
+
 | Minimum | Initial value | Maximum
Excitation type | 0 | 0 | 1
Delay length (ms) | 1 | 5 | 10
Feedback gain | -1 | 0.7 | 1

## Slide 4: Filters in the waveguide
 | Minimum | Initial value | Maximum
Exciter type | 0 | 0 | 1
Delay length (ms) | 1 | 5 | 10
Feedback | -1 | 0.9 | 1
Exciter cutoff (Hz) | 100 | 2000 | 10000
Loop cutoff (Hz) | 100 | 1200 | 10000
Filter
Filter
Feedbackgain
Output
+
Noise
burst
Delay

## Slide 5: Nonlinearities
 | Minimum | Initial value | Maximum
Exciter type | 0 | 0 | 1
Delay length (ms) | 1 | 5 | 10
Feedback | -2 | 0.7 | 2
Exciter cutoff (Hz) | 100 | 1000 | 10000
Loop cutoff (Hz) | 100 | 1000 | 10000
Filter
Filter
Sigmoid
Output
+
Noise
burst
Delay

## Slide 6: Controlling pitch
 | Minimum | Initial value | Maximum
Feedback | -2 | -1.1 | 2
Exciter cutoff (Hz) | 100 | 4000 | 10000
Loop cutoff (Hz) | 100 | 2300 | 10000
Filter
Filter
Sigmoid
Output
+
Noise
burst
Delay

## Slide 7: Note transitions
 | Minimum | Initial value | Maximum
Note | 0 | 0 | 3.9
Feedback | -2 | -1.1 | 2
Exciter cutoff (Hz) | 100 | 4000 | 10000
Loop cutoff (Hz) | 100 | 2300 | 10000
Filter
Filter
Sigmoid
Output
+
Noise
burst
Delay2
Crossfade
Delay1

## Slide 8: Animal vocalization example
 | Minimum | Initial value | Maximum
Control | 0 | 0.6 | 1
Excitation
Sigmoid
Tremolo
+
Output
Delay1
BP1
BP2
+

## Slide 9: Flute example
 | Minimum | Initial value | Maximum
Bandpass frequency (Hz) | 80 | 1100 | 4200
Lowpass frequency (Hz) | 80 | 3500 | 10000
Crossfade | 0 | 0.6 | 0.95
Feedback | -2 | 1.4 | 2
Exciter cutoff (Hz) | 80 | 700 | 10000
Excitation
Sigmoid
Crossfade
+
Output
Delay
BP
LP

## Slide 10: Common forms
Excitation
Delay
Feedbackgain
Output
+
Excitation
Delay
Feedbackgain
Output
+
Excitation
Delay
Feedbackgain
Output
+
Delay
A
B
C