## Slide 1: How it works
Generate short excitation waveform (length L samples), typically noise
Excitation is output & simultaneously fed back into delay line of L samples
  delay line acts to store one period of the signal
Output of delay line fed through filter
  Filter gain must be less than 1 at all frequencies, to avoid unstable feedback loop
  Filter typically a low order, lowpass filter
  Filter characteristics mainly determine harmonic structure of decaying tone.
Filtered output simultaneously mixed back into output & into delay line
loops short waveform through filtered delay line
Noise
burst
Delay
Lowpass filter
destination
+

## Slide 2: Simple implementation
Tuning the string
L is the number of samples of delay
So delay time D=L/fs
  D is the period, i.e. time before it repeats
Fundamental frequency should be 1/D
Want D very small
  10 ms  100 Hz
  5 ms  200 Hz
  2 ms  500 Hz
Noise
Noise
Gain
Delay
Feedback
Gain
destination
+
Variations
Can replace filter with just feedback gain
Can have excitation decay over short time

## Slide 3: Delay line with feedback
Input
Delay
Feedbackgain
Output
+
 | Minimum | Initial value | Maximum
Excitation type | 0 | 0 | 1
Delay length (ms) | 1 | 5 | 10
Feedback gain | -1 | 0.7 | 1

## Slide 4: Use audio worklet for feedback delay
Noise gain
Feedbackgain
Output
+
Noise
Delay
Noise gain
Feedbackdelay
Output
Noise

## Slide 5: KS from 1995 Valimaki
Loop filter
Output
Delay line
S(z)
y[n]
P(z)
x[n]
Pluck point
equaliser
Output
Input
String
model

## Slide 6: Smith 1992, fig 3 Ideal lossless waveguide with observation points at x=0 and x= 3X=3cT
z-1
z-1
z-1
y+[n]
y+[n-2]
y+[n-1]
y+[n-3]
y-[n]
y-[n+2]
y-[n+1]
y-[n+3]
x=0
z-1
z-1
z-1
+
+
x=cT
x=2cT
x=3cT
y[nT,3x]
y[nT,0]
…
…
…
…

## Slide 7: Smith 1992, fig 4 Simplified picture of ideal waveguide simulation
M samples delay
y+[n]
y+[n-M]
y-[n]
y-[n+M]
x=0
M samples delay
+
+
x=ζ
y[nT, ζ]
y[nT,0]
…
…
…
…
x=McT
z-M
x[n]
y[n]

## Slide 8: Filters in the waveguide
 | Minimum | Initial value | Maximum
Exciter type | 0 | 0 | 1
Delay length (ms) | 1 | 5 | 10
Feedback | -1 | 0.9 | 1
Exciter cutoff (Hz) | 100 | 2000 | 10000
Loop cutoff (Hz) | 100 | 1200 | 10000
Filter
Filter
Feedbackgain
Output
+
Noise
burst
Delay

## Slide 9: Nonlinearities
 | Minimum | Initial value | Maximum
Exciter type | 0 | 0 | 1
Delay length (ms) | 1 | 5 | 10
Feedback | -2 | 0.7 | 2
Exciter cutoff (Hz) | 100 | 1000 | 10000
Loop cutoff (Hz) | 100 | 1000 | 10000
Filter
Filter
Sigmoid
Output
+
Noise
burst
Delay

## Slide 10: Controlling pitch
 | Minimum | Initial value | Maximum
Feedback | -2 | -1.1 | 2
Exciter cutoff (Hz) | 100 | 4000 | 10000
Loop cutoff (Hz) | 100 | 2300 | 10000
Filter
Filter
Sigmoid
Output
+
Noise
burst
Delay

## Slide 11: Note transitions
 | Minimum | Initial value | Maximum
Note | 0 | 0 | 3.9
Feedback | -2 | -1.1 | 2
Exciter cutoff (Hz) | 100 | 4000 | 10000
Loop cutoff (Hz) | 100 | 2300 | 10000
Filter
Filter
Sigmoid
Output
+
Noise
burst
Delay2
Crossfade
Delay1

## Slide 12: Animal vocalization example
 | Minimum | Initial value | Maximum
Control | 0 | 0.6 | 1
Excitation
Sigmoid
Tremolo
+
Output
Delay1
BP1
BP2
+

## Slide 13: Flute example
 | Minimum | Initial value | Maximum
Bandpass frequency (Hz) | 80 | 1100 | 4200
Lowpass frequency (Hz) | 80 | 3500 | 10000
Crossfade | 0 | 0.6 | 0.95
Feedback | -2 | 1.4 | 2
Exciter cutoff (Hz) | 80 | 700 | 10000
Excitation
Sigmoid
Crossfade
+
Output
Delay
BP
LP

## Slide 14: Common forms
Excitation
Delay
Feedbackgain
Output
+
Excitation
Delay
Feedbackgain
Output
+
Excitation
Delay
Feedbackgain
Output
+
Delay
A
B
C

## Slide 15: Figure 1.2
ALT TEXT
Figure 1.2. A complex audio routing graph. It applies an envelope, filterbank, distortion and reverb to noise.
gainNode
BiquadNode
Peaking
BiquadNode
Lowshelf
BiquadNode
Peaking
BiquadNode
Highshelf
audioWorkletNode
whiteNoise
waveshaperNode
destination
convolverNode
setValueCurveAtTime
curve
buffer

## Slide 16: Figure 10.1
ALT TEXT
Figure 10.1. Magnitude response of a comb filter using 1 millisecond delay.
Chart: Frequency (Hz)

## Slide 17: Figure 10.2
ALT TEXT
Figure 10.2. Audio graph for Code example 10.2.
tone
toneGain
delay
feedback
destination

## Slide 18: Figure 10.3
ALT TEXT
Figure 10.3. Audio graph for a simple implementation of the Karplus-Strong algorithm.
Noise
Noise
Gain
Delay
Feedback
Gain
destination
+

## Slide 19: Figure 17.6
ALT TEXT
Figure 17.6 The spatialization procedure used in the PannerNode.
AudioListener
Input source
Distance
Sound cone
Panning
Left channel
Right channel
PannerNode parameters
panningModel
coneInnerAngle
coneOuterAngle
coneOuterGain
orientationX
orientationY
orientationZ
distanceModel
rolloffFactor
refDistance
maxDisrance
positionX
positionY
positionZ

## Slide 20: Figure 18.1
ALT TEXT
Figure 18.1. Interaction between an audio worklet node and audio worklet processor, along with the syntax for how these components can be created.
Asynchronous messaging
AudioWorkletProcessor
AudioWorklet global scope
Audio in
Audio out
registerProcessor('my-processor',
class extends
AudioWorkletProcessor {…}
)
AudioWorkletNode
Main global scope
Application interaction
let myNode = new AudioWorkletNode(
context,
'my-processor'
)

## Slide 21: Figure 19.1
ALT TEXT
Figure 19.1. Rewriting a buffer to store previous inputs.
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
x[14]
0
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
0
0
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]